## Slide 1: Sub-Kelvin Cooling Options for PICO
Peter Shirron
Cryogenics and Fluids Group, Code 552
NASA/Goddard Space Flight Center
Greenbelt, MD 20771 USA

## Slide 2: Sub-Kelvin Cooling Options
4He JT
3He JT
3He sorption cooler
Open cycle DR
NIS chip
Single-stage ADR
Helium Dewar
4He sorption cooler
Closed cycle DR
Two-stage ADR
Multi-stage ADR (single-shot and continuous)
Turbo Brayton
Pulse tube cooler
Primary coolers
Sub-kelvin
TRL 4
Single-stage ADR
TRL 6

## Slide 3: Continuous Sub-Kelvin Coolers
Dilution Refrigerator
  Open-cycle DR: Planck
  Closed-cycle DR: under development for Athena
Adiabatic Demagnetization Refrigerator
  3-stage ADR (continuous plus single-shot): Astro-H
  Continuous ADRs for cooling at ~1 K and ≤100 mK
Tentative PICO requirements
  16 µW at 100 mK
  ~1 mW at 1 K
    Temperature to be optimized based on eventual instrument details

## Slide 4: Planck OCDR
Open cycle version is first to work in zero-g
  Continuous, stable T, low cold mass
Launched in May 2009, operated for 2.6 years
Courtesy Gerard Vermeulen
Planck Cooling System
JT
expansion
300 K
Mixing is equivalent to evaporation of 3He

## Slide 5: OCDR Concept
Planck Performance:
Cooling power: 0.2 𝜇W at 100 mK
Lifetime: 2.5 years
Helium flow rate:
    3He 6 𝜇mol/s
    4He 18 𝜇mol/s
High pressure storage on satellite:
    3He 12 m3 STP
    4He 36 m3 STP
Scaling to lower temperature and higher cooling power results in excessive mass
- Need to close the cycle
Auxiliary cooler
JT
expansion
300 K
Notes: This cooler provided 0.2 microWatt at 100 mK in a 100% duty
In order to reach this performance, the flow rates of 3He and 4He were adjusted to 6 and 18 micromol/s. The life time of 2.5 years is set by the initial amount of fluids stored on the satellite.

## Slide 6: Closed Cycle Dilution Refrigerator
Key Features:
Still with a liquid-vapor interface in zero-g
4He circulation with fountain pump
External pump for 3He circulation
Optimized CFHXs to go below 50 mK
Requires auxiliary cooling at 4.2 K and 1.7 K
Benefits:
  Continuous cooling
  No magnetic fields
  Multiple fixed temperature heat intercepts
External 3He pump
Notes: Here are summarized the technical key points to developed the closed cycles dilution refrigerator.

## Slide 7: Prototype Closed Cycle DR
53.4 mK with 1.0 𝜇W load
  0.8-1.2 𝜇W
5-6 𝜇W at 100 mK
40 𝜇W at 300 mK on CFHX 2-3 junction
Performance
3He pump outside cryostat
Simulated 1.7 K interface with pumped pot
Test conditions
JAXA or U. Twente 3He pump
JAXA 1.7 K cryocooler
Improved heat exchangers
Critical steps for EM
Notes: Here is a picture and a schematic of this last prototype. We can see the different components I've been talking about.
We can notice large thermal anchors at low temperature to improve temperature stability and a structure made of carbon tubes to test future materials.

## Slide 8: ADR Cycle
Adiabatic magnetization
Isothermal magnetization
Adiabatic demagnetization
Isothermal demagnetization
Based on the magnetocaloric effect
  Paramagnetic materials will warm/cool under influence of increasing/decreasing magnetic field
Inherently single-shot, BUT… reversible, so intrinsically high efficiency

## Slide 9: Continuous Cooling with an ADR
Two (or more) stages can be used to generate continuous cooling
Two configurations
  Serial
    Heat is cascaded through upper stage(s)
  Parallel
    Stages alternate role in cooling load and rejecting heat
4-stage CADR
High efficiency of ADRs gives maximum
f~0.3
f~0.6-0.7

## Slide 10: Proposed PICO ADR configuration
2-stage parallel CADR operating at 1 K
3-stage series CADR operating at 0.1 K

## Slide 11: 2-Stage Parallel CADR
Heat rejection at 4.5 K
Stages equivalent to upper stages built for Astro-H
Cooling power depends on available cooling at 4.5 K
  Nominal total is 40 mW
  Astro-H: 10 mW static load
2-stage series CADR demonstrated on Astro-H
  ~1 mW at 1.5 K

## Slide 12: 3-Stage Series CADR
Performance will exceed that obtained for the 4-stage CADR
  Lower parasitic heat loads

## Slide 13: Temperature Stability at 100 mK
Periodic heat flows can generate temperature disturbances at cold stages
Options for reducing magnitude of disturbances
  Reduce cycle speed -> reduces cooling power
  Feedforward control: use knowledge of changes in heat flow to calculate changes in magnetization rate

## Slide 14: Temperature Stability at 1 K
Astro-H 2-stage series CADR operated at 1.5 K
  Only demonstrated on the ground (no cryogen-free operation during mission)

## Slide 15: Summary
PICO requirements: 16 µW at 100 mK, ~1 mW at 1 K
Open-cycle DR
  Critical functionality of the dilution unit has been demonstrated (TRL 4)
  Cooling power not quite at level needed for Athena (1 µW at 50 mK), or PICO (5-6 µW at 100 mK)
  Requires auxiliary cooling at 1.7 K and 4.5 K
Continuous ADRs
  Only high TRL cooler that has demonstrated continuous cooling with suitable cooling power for PICO
  Only requires auxiliary cooling at 4.5 K
  Architecture is very flexible
    Addition of stages can
      Improved temperature stability
      Add constant temperature nodes
      Improve cooling power (by increasing average heat reject rate)